## Slide 1: Fluid Kinematics
Fluid Mechanics
December 18, 2012

## Slide 2: Fluid Flow Concepts and Reynolds Transport Theorem
Descriptions of:
  fluid motion
  fluid flows
  temporal and spatial classifications
Analysis Approaches
  Lagrangian vs. Eulerian
Moving from a system to a control volume
  Reynolds Transport Theorem

## Slide 3: Descriptions of Fluid Motion
Defined as particle moves (over time)
Defined instantaneously
  streamline
    has the direction of the velocity vector at each point
    no flow across the streamline
    steady flow streamlines are fixed in space
    unsteady flow streamlines move
  pathline
    path of a particle
    same as streamline for steady flow
  streakline
    tracer injected continuously into a flow
    same as pathline and streamline for steady flow
Draw Streamlines
Unsteady demo

## Slide 4: Descriptors of Fluid Flows
  Laminar flow
    fluid moves along smooth paths
    viscosity damps any tendency to swirl or mix
  Turbulent flow
    fluid moves in very irregular paths
    efficient mixing
    velocity at a point fluctuates

## Slide 5: Temporal/Spatial Classifications
If averaged over a suitable time
Steady - unsteady
Uniform - nonuniform
Can turbulent flow be steady? _______ ________________ ________________
Changing in time
Changing in space

## Slide 6: Analysis Approaches
  Lagrangian (system approach)
    Describes a defined _____ (position, velocity, acceleration, pressure, temperature, etc.) as functions of time
    Track the location of a migrating bird
  Eulerian
    Describes the flow ______ (velocity, acceleration, pressure, temperature, etc.) as functions of position and time
    Count the birds passing a particular location
If you were going to study water flowing in a pipeline, which approach would you use? ____________
Eulerian
mass
field

## Slide 7: The Dilemma
The laws of physics in their simplest forms describe systems (the Lagrangian approach)
  Conservation of Mass, Momentum, Energy
It is impossible to keep track of the system in many fluids problems
The laws of physics must still hold in a Eulerian world!
We need some tools to bridge the gap

## Slide 8: Reynolds Transport Theorem
A moving system flows through the fixed control volume
The moving system transports extensive properties across the control volume surfaces
We need a bookkeeping method to keep track of the properties that are being transported into and out of the control volume

## Slide 9: Control Volume Conservation Equation
per unit mass
Total amount of some property
B =__________________________ in the system
b = Amount of the property ___________
=
+
Rate of increase of the property in the system
Rate of increase of the property in the control volume
Rate of efflux of the property across the control volume boundary

## Slide 10: Summary
Reynolds Transport Theorem can be applied to a control volume of finite size
  We don’t need to know the flow details within the control volume!
  We do need to know what is happening at the control surfaces.
Conservation of mass (for all species)
Newton’s 2nd law of motion (momentum) _______
First law of thermodynamics (energy)
F = ma

## Slide 11: Control Volume Conservation Equation
0 = -1 + (-0 + 1)
0 = 1 + (-1 + 0)
0 = 0 + (-0 + 0)

## Slide 12: Mt. St. Helens

## Slide 13: Application of Reynold’s Transport Theorem
Chemical with concentration Cin enters reactor with flow rate Q and exits with concentration C.
Chemical decays at rate kC
What is b? What is B?
What is rb?
What is left side of equation?
What is ?
C/r
CV
C