## Slide 1: Types of Aqueducts used in the Catskill System
Back to Aqueducts

## Slide 2: Types of Aqueducts on Hydraulic Grade
following natural surface
  open channel
  cut-and-cover
above natural surface
  embankment
  viaduct
below natural surface
  grade tunnel
Back to Aqueducts

## Slide 3: Types of Aqueducts below Hydraulic Grade
Following or above natural surface
  wooden pipe
  reinforced concrete pipe
  steel pipe
  plastic pipe
below natural surface
  pressure tunnel
Back to Aqueducts

## Slide 4: Profile of Catskill Aqueduct
Small Scale profile of Catskill Aqueduct, Ashokan Reservoir to Silver Lake Reservoir. (White p. 46)
Back to Aqueducts

## Slide 5: Cross-section of Cut-and-cover Aqueduct
Construction of cover embankment. Rock was usually excavated to a 6 on 1 slope. Minimum thickness of concrete along sides 20 ins., but usually thicker owing to disintegrated condition of surface rocks. (White p. 50)
Back to Aqueducts

## Slide 6: Construction of Cut-and-cover aqueduct
Shows steel form and carriage; also locomotive crane used to place concrete, move outside forms, and assist in excavation. (White p. 220)
Back to Aqueducts

## Slide 7: Electric carriage for moving interior forms
Carriage and upper jacks are motor driven. Side jacks and turntable hand driven. (White p. 221)
Back to Aqueducts

## Slide 8: Traveling aqueduct building plant
Traveling crushing concrete, mixing, and form-moving plant completing last section of aqueduct adjoining shaft 1 of contract 12. This plant built 7500 feet of aqueduct in two seasons. (White p. 223)
Back to Aqueducts

## Slide 9: Cut-and-cover Arch
This section was
cast between steel
forms with steel plate in expansion joints at 60-ft intervals. Steel plates 6” x 3/8” were places in both invert and arch joints to act as water stops. (White p. 236)
Back to Aqueducts

## Slide 10: Steel forms and locomotive crane
Continuous method was here used, forms being used “telescoping.” 60- to 75-foot section concreted daily. (White p. 374)
Back to Aqueducts

## Slide 11: Cut-and-cover Aqueduct on Curve
Arch cast with aid of steel forms built wedge-shaped in 5-foot lengths to 200 feet radius. Section 17 feet high by 17 feet 6 inches wide. (White p. 237)
Back to Aqueducts

## Slide 12: Peak Tunnel (grade tunnel) ready for concrete lining
Footing courses are in place. Center track for hauling material to upper portion of contract 11. Tunnel is 3450 feet long on tangent.(White p. 243)
Back to Aqueducts

## Slide 13: Completed pressure tunnel lining
Note smooth finish and close joints at invert and springing line. Concrete surface very dry under ground water bend. (White p. 331)
Back to Aqueducts

## Slide 14: Hunters Brook Steel Pipe Siphon
Laying of steel pipe on concrete pedestal blocks. Later pipe was filled with water, covered with concrete and earth and lined with 2 ins. of mortar. (White p. 467)
Back to Aqueducts

## Slide 15: Hudson River Crossing
View from West Point of Hudson River at Storm King and Breakneck, where Catskill Aqueduct Crosses 1100 feet below surface of river. (White p. 406)
Back to Aqueducts