## Slide 1: Finite Control Volume Analysis
CEE 331
September 7, 2015
Application of Reynolds Transport Theorem

## Slide 2: Moving from a System to a Control Volume
Mass
Linear Momentum
Moment of Momentum
Energy
Putting it all together!

## Slide 3: Conservation of Mass
B = Total amount of ____ in the system
b = ____ per unit mass = __
mass
1
mass
But DMsys/Dt = 0!
cv equation
mass leaving - mass entering = - rate of increase of mass in cv
Continuity Equation

## Slide 4: Conservation of Mass
1
2
V1
A1
If mass in cv is constant
Unit vector is ______ to surface and pointed ____ of cv
normal
out
We assumed uniform ___ on the control surface
r
is the spatially averaged velocity normal to the cs
[M/T]

## Slide 5: Continuity Equation for Constant Density and Uniform Velocity
Density is constant across cs
Density is the same at cs1 and cs2
[L3/T]
Simple version of the continuity equation for conditions of constant density. It is understood that the velocities are either ________ or _______ ________.
uniform
spatially averaged

## Slide 6: Example: Conservation of Mass?
The flow out of a reservoir is 2 L/s. The reservoir surface is 5 m x 5 m. How fast is the reservoir surface dropping?
h
Example
Constant density
Velocity of the reservoir surface

## Slide 7: Linear Momentum Equation
cv equation
momentum
momentum/unit mass
Steady state
This is the “ma” side of the F = ma equation!
Vectors!

## Slide 8: Linear Momentum Equation
Assumptions
Vectors!!!
Uniform density
Uniform velocity
V  A
Steady
V fluid velocity relative to cv

## Slide 9: Steady Control Volume Form of Newton’s Second Law
What are the forces acting on the fluid in the control volume?
Gravity
Shear at the solid surfaces
Pressure at the solid surfaces
Pressure on the flow surfaces
Why no shear on control surfaces? _______________________________
No velocity tangent to control surface

## Slide 10: Resultant Force on the Solid Surfaces
The shear forces on the walls and the pressure forces on the walls are generally the unknowns
Often the problem is to calculate the total force exerted by the fluid on the solid surfaces
The magnitude and direction of the force determines
  size of _____________needed to keep pipe in place
  force on the vane of a pump or turbine...
=force applied by solid surfaces
thrust blocks

## Slide 11: Linear Momentum Equation
The momentum vectors have the same direction as the velocity vectors
Fp1
Fp2
W
M1
M2
Fssy
Fssx
Forces by solid surfaces on fluid

## Slide 12: Example: Reducing Elbow
Reducing elbow in vertical plane with water flow of 300 L/s. The volume of water in the elbow is 200 L.
Energy loss is negligible.
Calculate the force of the elbow on the fluid.
W = ________________________
section 1 section 2
D 50 cm 30 cm
A ____________ ____________
V ____________ ____________
p 150 kPa ____________
M ____________ ____________
Fp ____________ ____________
1
2
1 m
z
x
Direction of V vectors
0.196 m2
0.071 m2
1.53 m/s ↑
4.23 m/s →
-459 N ↑
1270 N →
29,400 N ↑
-rg*volume=-1961 N ↑
?
?←

## Slide 13: Example: What is p2?
P2 = 132 kPa
Fp2 = 9400 N

## Slide 14: Example: Reducing Elbow Horizontal Forces
1
2
Fluid is pushing the pipe to the ______
left
z
x
Force of pipe on fluid
Fp2
M2

## Slide 15: Example: Reducing Elbow Vertical Forces
1
2
Pipe wants to move _________
up
z
x
Fp1
M1
W
28 kN acting downward on fluid

## Slide 16: Example: Fire nozzle
A small fire nozzle is used to create a powerful jet to reach far into a blaze. Estimate the force that the water exerts on the fire nozzle. The pressure at section 1 is 1000 kPa (gage). Ignore frictional losses in the nozzle.
8 cm
2.5 cm

## Slide 17: Fire nozzle: Solution
Identify what you need to know
Determine what equations you will use
8 cm
2.5 cm
1000 kPa
P2, V1, V2, Q, M1, M2, Fss
Bernoulli, continuity, momentum

## Slide 18: Find the Velocities
continuity→

## Slide 19: Fire nozzle: Solution
2.5 cm
8 cm
1000 kPa
force applied by nozzle on water
Is Fssx the force that the firefighters need to brace against? ____ __________
Which direction does the nozzle want to go? ______
NO!
Moments!

## Slide 20: Example: Momentum with Complex Geometry
cs1
cs3
q1
q2
cs2
Find Q2, Q3 and force on the wedge in a horizontal plane.
x
y
q3
Unknown: ________________
Q2, Q3, V2, V3, Fx

## Slide 21: 5 Unknowns: Need 5 Equations
cs1
cs3
q1
cs2
x
y
q3
Unknowns: Q2, Q3, V2, V3, Fx
Continuity
Bernoulli (2x)
Momentum (in x and y)
q2
Identify the 5 equations!

## Slide 22: Solve for Q2 and Q3
x
y
q
Component of velocity in y direction
Mass conservation
Negligible losses – apply Bernoulli
atmospheric pressure

## Slide 23: Solve for Q2 and Q3
Why is Q2 greater than Q3?
Eliminate Q3
+
+
-

## Slide 24: Solve for Fssx
Force of wedge on fluid

## Slide 25: Vector solution

## Slide 26: Vector Addition
cs1
cs3
q1
q2
cs2
x
y
q3
Where is the line of action of Fss?

## Slide 27: Moment of Momentum Equation
cv equation
Moment of momentum
Moment of momentum/unit mass
Steady state

## Slide 28: Application to Turbomachinery
r2
r1
Vn
Vt
cs1
cs2
rVt
Vn

## Slide 29: Example: Sprinkler
Total flow is 1 L/s.
Jet diameter is 0.5 cm.
Friction exerts a torque of 0.1 N-m-s2 w2.
q = 30º.
Find the speed of rotation.
vt
w
10 cm
q
Vt and Vn are defined relative to control surfaces.
cs2

## Slide 30: Example: Sprinkler
= 34 rpm
c = -(1000 kg/m3)(0.001 m3/s)2(0.1m)(2sin30)/3.14/(0.005 m)2
b = (1000 kg/m3)(0.001 m3/s) (0.1 m) 2 = 0.01 Nms
c = -1.27 Nm
w = 3.5/s
a = 0.1Nms2
Reflections
What is w if there is no friction? ___________
What is Vt if there is no friction ?__________
w = 127/s
0

## Slide 31: Energy Equation
cv equation
First law of thermodynamics: The heat QH added to a system plus the work W done on the system equals the change in total energy E of the system.
What is for a system?
DE/Dt

## Slide 32: dE/dt for our System?
Heat transfer
Shaft work
Pressure work

## Slide 33: General Energy Equation
z
cv equation
1st Law of Thermo
Potential
Kinetic
Internal (molecular spacing and forces)
Total

## Slide 34: Simplify the Energy Equation
Steady
Assume...
But V is often ____________ over control surface!
Hydrostatic pressure distribution at cs
ŭ is uniform over cs
not uniform
0

## Slide 35: Energy Equation: Kinetic Energy
If V tangent to n
kinetic energy correction term
V = point velocity
V = average normal velocity over cs
a = _________________________
a =___ for uniform velocity
1

## Slide 36: Energy Equation: steady, one-dimensional, constant density
mass flux rate

## Slide 37: Energy Equation: steady, one-dimensional, constant density
hP
Lost mechanical energy
divide by g
mechanical
thermal

## Slide 38: Thermal Components of the Energy Equation
Example
Water specific heat = 4184 J/(kg*K)
For incompressible liquids
Change in temperature
Heat transferred to fluid

## Slide 39: Example: Energy Equation (energy loss)
datum
2 m
4 m
An irrigation pump lifts 50 L/s of water from a reservoir and discharges it into a farmer’s irrigation channel. The pump supplies a total head of 10 m. How much mechanical energy is lost?
2.4 m
cs1
cs2
hL = 10 m - 4 m
What is hL?
Why can’t I draw the cs at the end of the pipe?

## Slide 40: Example: Energy Equation (pressure at pump outlet)
datum
2 m
4 m
50 L/s
hP = 10 m
The total pipe length is 50 m and is 20 cm in diameter. The pipe length to the pump is 12 m. What is the pressure in the pipe at the pump outlet? You may assume (for now) that the only losses are frictional losses in the pipeline.
2.4 m
We need _______ in the pipe, __, and ____ ____.
cs1
cs2
0
/
0
/
0
/
0
/
velocity
a
head loss

## Slide 41: Example: Energy Equation (pressure at pump outlet)
Expect losses to be proportional to length of the pipe
hl = (6 m)(12 m)/(50 m) = 1.44 m
V = 4(0.05 m3/s)/[ p(0.2 m)2] = 1.6 m/s
How do we get the velocity in the pipe?
How do we get the frictional losses?
What about a?
Q = VA
A = pd2/4
V = 4Q/( pd2)

## Slide 42: Kinetic Energy Correction Term: a
a is a function of the velocity distribution in the pipe.
For a uniform velocity distribution ____
For laminar flow ______
For turbulent flow _____________
  Often neglected in calculations because it is so close to 1
a is 1
a is 2
1.01 < a < 1.10

## Slide 43: Example: Energy Equation (pressure at pump outlet)
datum
2 m
4 m
50 L/s
hP = 10 m
V = 1.6 m/s
a = 1.05
hL = 1.44 m
2.4 m
= 59.1 kPa

## Slide 44: Example: Energy Equation (Hydraulic Grade Line - HGL)
pipe burst
We would like to know if there are any places in the pipeline where the pressure is too high (_________) or too low (water might boil - cavitation).
Plot the pressure as piezometric head (height water would rise to in a piezometer)
How?

## Slide 45: Example: Energy Equation (Energy Grade Line - EGL)
datum
2 m
4 m
50 L/s
2.4 m
HP = 10 m
p = 59 kPa
What is the pressure at the pump intake?
Entrance loss
Exit loss
Loss due to shear

## Slide 46: EGL (or TEL) and HGL
Pressure head (w.r.t. reference pressure)
velocity
head
Elevation head (w.r.t. datum)
Piezometric head
Energy Grade Line
Hydraulic Grade Line
What is the difference between EGL defined by Bernoulli and EGL defined here?

## Slide 47: EGL (or TEL) and HGL
pump
coincident
reference pressure
The energy grade line may never slope upward (in direction of flow) unless energy is added (______)
The decrease in total energy represents the head loss or energy dissipation per unit weight
EGL and HGL are ____________and lie at the free surface for water at rest (reservoir)
Whenever the HGL falls below the point in the system for which it is plotted, the local pressures are lower than the __________________

## Slide 48: Example HGL and EGL
z
z = 0
pump
energy grade line
hydraulic grade line
velocity head
pressure head
elevation
datum

## Slide 49: Bernoulli vs. Control Volume Conservation of Energy
Free jet
pipe
Find the velocity and flow. How would you solve these two problems?

## Slide 50: Bernoulli vs. Control Volume Conservation of Energy
Point to point along streamline
Control surface to control surface
No frictional losses
Has a term for frictional losses
Based on velocity
Requires kinetic energy correction factor
Includes shaft work
Based on velocity
Has direction!
point
average

## Slide 51: Power and Efficiencies
Electrical power
Shaft power
Impeller power
Fluid power
EI
Tw
Tw
gQHp
Motor losses
bearing losses
pump losses
Prove this!
P = FV

## Slide 52: Example: Hydroplant
Powerhouse
River
Reservoir
Penstock
Q = 5 m3/s
2100 kW
180 rpm
116 kN·m
50 m
Water power =
Overall efficiency =
efficiency of turbine =
efficiency of generator =
solution
0.857
0.893
0.96
2.45 MW

## Slide 53: Energy Equation Review
Control Volume equation
Simplifications
  steady
  constant density
  hydrostatic pressure distribution across control surface (streamlines parallel)
Direction of flow matters (in vs. out)
We don’t know how to predict head loss

## Slide 54: Conservation of Energy, Momentum, and Mass
Most problems in fluids require the use of more than one conservation law to obtain a solution
Often a simplifying assumption is required to obtain a solution
  neglect energy losses (_______) over a short distance with no flow expansion
  neglect shear forces on the solid surface over a short distance
to heat
mechanical

## Slide 55: Head Loss: Minor Losses
greater
Head (or energy) loss due to: outlets, inlets, bends, elbows, valves, pipe size changes
Losses due to expansions are ________ than losses due to contractions
Losses can be minimized by gradual transitions
Losses are expressed in the form where KL is the loss coefficient
When V, KE  thermal

## Slide 56: Head Loss due to Sudden Expansion: Conservation of Energy
zin = zout
Relate Vin and Vout?
in
out
Relate pin and pout?
Mass
Momentum
Where is p measured?___________________________
At centroid of control surface
z
x

## Slide 57: Head Loss due to Sudden Expansion: Conservation of Momentum
Apply in direction of flow
Neglect surface shear
Divide by (Aout g)
Pressure is applied over all of section 1.
Momentum is transferred over area corresponding to upstream pipe diameter.
Vin is velocity upstream.
1
2
A1
A2
x

## Slide 58: Head Loss due to Sudden Expansion
Discharge into a reservoir?_________
Energy
Momentum
Mass
KL=1
2
2
2

## Slide 59: Pressure recovery in Manifolds
Is there pressure recovery in a manifold that has water exiting the manifold through side ports?
Velocity in the manifold is decreasing. Is kinetic energy converted to pressure?

## Slide 60: Head Loss due to reduced flow caused by side port outlet
Apply in direction of flow
Neglect surface shear
1
2
x

## Slide 61: Head Loss due to deceleration
Energy
Momentum
1
2
x
This analysis is incorrect.
Shows negative energy loss…
Must add term for energy lost through side port

## Slide 62: Jet expansion in a confined channel: pressure recovery?
Is there pressure recovery in a hydraulic flocculator?

## Slide 65: Example: Losses due to Sudden Expansion in a Pipe (Teams!)
A flow expansion discharges 0.5 L/s directly into the air. Calculate the pressure immediately upstream from the expansion
1 cm
3 cm
We can solve this using either the momentum equation or the energy equation (with the appropriate term for the energy losses)!
Solution
Use the momentum equation…

## Slide 66: Scoop
A scoop attached to a locomotive is used to lift water from a stationary water tank next to the train tracks into a water tank on the train. The scoop pipe is 10 cm in diameter and elevates the water 3 m.
Draw several streamlines in the left half of the stationary water tank (use the scoop as your frame of reference) including the streamlines that attach to the submerged horizontal section of the scoop.
Use the streamlines to help you draw a control volume and clearly label the control surfaces.
How fast must the locomotive be moving (Vscoop) to get a flow of 4 L/s if the frictional losses in the pipe are equal to 1.8 V2/2g where V is the average velocity of the water in the pipe. (Vscoop = 7.7 m/s)

## Slide 67: Scoop
Q = 4 L/s
d = 10 cm
3 m
stationary water tank
Vscoop

## Slide 68: Scoop Problem: ‘The Real Scoop’
moving water tank
Bernoulli
Energy

## Slide 69: Summary
Control volumes should be drawn so that the surfaces are either tangent (no flow) or normal (flow) to streamlines.
In order to solve a problem the flow surfaces need to be at locations where all but 1 or 2 of the energy terms are known
When possible choose a frame of reference so the flows are steady

## Slide 70: Summary
Control volume equation: Required to make the switch from Lagrangian to Eulerian
Any conservative property can be evaluated using the control volume equation
  mass, energy, momentum, concentrations of species
Many problems require the use of several conservation laws to obtain a solution
end

## Slide 71: Scoop Problem
stationary water tank

## Slide 72: Scoop Problem: Change your Perspective
moving water tank

## Slide 73: Scoop Problem: Be an Extremist!
Very short riser tube
Very long riser tube

## Slide 74: Example: Conservation of Mass (Team Work)
The flow through the orifice is a function of the depth of water in the reservoir
Find the time for the reservoir level to drop from 10 cm to 5 cm. The reservoir surface is 15 cm x 15 cm. The orifice is 2 mm in diameter and is 2 cm off the bottom of the reservoir. The orifice coefficient is 0.6.
CV with constant or changing mass.
Draw CV, label CS, solve using variables starting with to integration step

## Slide 75: Example Conservation of Mass Constant Volume
h
cs1
cs2

## Slide 76: Example Conservation of Mass Changing Volume
h
cs1
cs2

## Slide 77: Example Conservation of Mass

## Slide 78: Pump Head
hp

## Slide 79: Example: Venturi

## Slide 80: Example: Venturi
Find the flow (Q) given the pressure drop between section 1 and 2 and the diameters of the two sections. Draw an appropriate control volume. You may assume the head loss is negligible. Draw the EGL and the HGL.
1
2
Dh

## Slide 81: Example Venturi

## Slide 82: Reflections
What is the name of the equation that we used to move from a system (Lagrangian) view to the control volume (Eulerian) view?
Explain the analogy to your checking account.
The velocities in the linear momentum equation are relative to …?
When is “ma” non-zero for a fixed control volume?
Under what conditions could you generate power from a rotating sprinkler?
What questions do you have about application of the linear momentum and momentum of momentum equations?

## Slide 83: Temperature Rise over Taughanock Falls
Drop of 50 meters
Find the temperature rise
Ignore kinetic energy

## Slide 84: Hydropower

## Slide 85: Solution: Losses due to Sudden Expansion in a Pipe
A flow expansion discharges 0.5 L/s directly into the air. Calculate the pressure immediately upstream from the expansion
1 cm
3 cm
Carburetors and water powered vacuums